## Slide 1: Pulser: Fast Congestion Response Using Explicit Incast Notifications for Datacenter Networks
Hamidreza Almasi, Hamed Rezaei, Muhammad Usama Chaudhry, Balajee Vamanan

## Slide 2: Datacenters host a mix of applications
Low Latency
High Bandwidth
Shallow Buffers
Large Scale

## Slide 3: Goal: Joint optimization of short flows’ completion times and long flows’ throughput
Key: Accurately and quickly respond to congestion
Heavy-tailed datacenter traffic
  Small fraction of long flows account for most bytes
Growing popularity of online services
Low tail latency
High throughput
Problem: Incast, synchronized bursts of short flows

## Slide 4: Traditional TCP cannot infer congestion quickly
Timeout
Congestion
Cwnd = 1 MSS
High FCT
&
Low Throughput

## Slide 5: Contributions
A combination of in-network and end-host mechanisms
  Explicitly detect and isolate incast congestion
Novel gradient-based incast detection algorithm
Pulser: leverages detection algorithm to improve:
  Short flows’ completion time
  Long flows’ throughput
Up to 70% reduction in percentile FCT without throughput loss

## Slide 6: Outline
Introduction
Background and existing solutions
Our proposal: Pulser
Methodology and key results
Conclusion

## Slide 7: Related work
DCTCP: Infers the congestion faster than TCP
  Switches mark packets with ECN if their buffer builds up
    Instantaneous queue length > ECN Threshold → Mark
    Senders sending rate ∝ Number of marked packets
Receiver
Switch
Sender 2
Sender 1
Time
Time
cwnd
Qlen
ECN Threshold
1 RTT
1 MSS
Mark packets

## Slide 8: DCTCP: iterative, gradual window adaptation
DCTCP responds to congestion faster than traditional TCP
BUT,
During severe incast, network queues build up at much faster rate…
DCTCP has iterative, gradual window adaptation → Packet drop
Sender 1
Sender 2
Sender 3
Sender 4
Receiver
Insight:
It is necessary to drastically slow down all senders during incast in order to avoid packet loss

## Slide 9: Related work (cont’d)
ICTCP
Receiver side detection & no network support → Slow
RCP
Only observing intervening flows’ rates → No incast isolation
TIMELY
RTT-based, end-host implementation & Not customized for incast
DCQCN
Rate-based, leverages ECN for RDMA
QCN
Ethernet layer → Not applicable to large L3 routing datacenters
ExpressPass and NDP
Receiver-driven proposals

## Slide 10: Outline
Introduction
Background and existing solutions
Our proposal: Pulser
Methodology and key results
Conclusion

## Slide 11: Pulser: Explicitly detect and isolate incast congestion
hand-in-hand Incast detection and aggressive response
Without sacrificing the throughput

## Slide 12: Pulser design: Fast and accurate incast detection
Explicit Incast Notification (EIN)
  Algorithm marks packets if gradient of queue length exceeds a threshold
  EIN requires:
    An additional bit in IP header
    Another bit in TCP header of ACKs to notify senders
Switch egress queue
= =

## Slide 13: Pulser design: Fast and accurate incast detection
Main parameters:
Not independent
  Inversely related
  Also depend on the nature of incast
    Short incasts → Smaller to quickly react
    Long incasts → Larger N to avoid false positives and throughput loss
  Rule of thumb*: Set based on typical incast duration
    of incasts last less than →
* Zhang, Qiao, et al. "High-resolution measurement of data center microbursts." in IMC 2017

## Slide 14: Pulser design: Congestion control
Pulser sender
EIN
1
2

## Slide 15: Outline
Introduction
Background and existing solutions
Our proposal: Pulser
Methodology and key results
Conclusion

## Slide 16: Experimental methodology
Simulation:
  ns-3 simulator
  Leaf-spine topology
    400 servers, 20 leaf and 10 spine switches, each leaf connected to 20 servers
    Oversubscription factor: 2
    links
    RTT
  Workloads:
    Poisson flow arrivals between random source and destinations
    Short flow sizes randomly chosen between 8 KB to 32 KB
    1 MB long flows

## Slide 17: Results: Flow Completion Time (FCT)
Median FCT
Tail (99th %-ile) FCT
On average, compared to DCTCP and ICTCP
  Load > 20%:
    50% reduction
  Higher loads:
    Up to 70% reduction
On average, compared to DCTCP and ICTCP
  Load > 20%:
    10% reduction
  Higher loads:
    Up to 25% reduction
DC apps are more sensitive to tail FCT
& Pulser makes the right trade-off
Incast congestion is an issue at higher loads

## Slide 18: Results: Throughput
Long flow throughput decreases with load due to increased congestion
Pulser’s ON/OFF window modulation helps both at the beginning and the end of incast
16% and 22% higher throughput compared to ICTCP and DCTCP respectively

## Slide 19: Results: Queue length and congestion window behavior
Incast starts at t=120 and finishes at t=300
Pulser instantly backs off and recovers while DCTCP oscillates around
Load = 60%
Pulser reduces queue buildup by as much as 50%

## Slide 20: Results: Sensitivity of tail FCT to incast degree
Incast degree varied as 24 (default), 32 and 40
Results normalized to default case
At least 2x improvement over DCTCP and ICTCP for 60% and 80% loads
Performance improvement robust for a range of loads and incast degrees

## Slide 21: Real implementation
Metric | DCTCP | Pulser
Avg. flow completion time (s) | 1.99 | 1.59
99th percentile flow completion time (s) | 13.32 | 9.85
Throughput (Mbps) | 28 | 35
Rate limited to 50 Mbps
Aggregator
8 VMs,
Each NIC rate limited to 50 Mbps
Physical switch
Linux switch
Iperf3 to generate:
1 background 40MB long flow
15 synchronous bursts of short 100KB flows
Senders
Senders

## Slide 22: Outline
Introduction
Background and existing solutions
Our proposal: Pulser
Methodology and key results
Conclusion

## Slide 23: Conclusion
Prior congestion control approaches do not explicitly detect and isolate incast
  Existing end-host mechanisms cannot aggressively respond without throughput loss
We propose:
  EIN: gradient-based incast detection at network switches which is fast and accurate
  Pulser: congestion control scheme which
    Quickly backs off during incast for short time intervals without hurting latency
    Restores the rate after the incast without losing throughput
Future work
  Learning the incast characteristics in different environments and adapting pulses accordingly (e.g. tailor pulse duration to the gradient extent)
  Evaluating Pulser on large production datacenter traces