## Slide 1: ResQueue: A Smarter Datacenter Flow Scheduler
Hamed Rezaei and Balajee Vamanan
hrezae2@uic.edu
University of Illinois at Chicago

## Slide 2: Outline
Introduction to datacenter networks
Challenge: Incast problem in datacenter networks
ResQueue: Results
Our proposal: ResQueue
Conclusion
Idea and opportunity

## Slide 3: Datacenter traffic characteristics
Datacenters host diverse applications; produce mixed traffic patterns
  Foreground applications
    Respond to user queries (e.g., Web search, social networks)
      Short flows (e.g., < 10 KB)
      Sensitive to higher percentiles of Flow Completion Times (FCT)
      Produce most flows
  Background applications
    Update/backup/data replication (e.g., VM migration)
      Long flows (e.g., > 10 MB)
      Sensitive to throughput
      Produce most load

## Slide 4: Goal: Joint optimization of short flows’ completion times and long flows’ throughput
Key: Accurately and quickly respond to congestion
  Most flows are short  Short flows cause congestion
Growing popularity of online services
Low tail latency
High throughput
Problem: Incast of short flows!

## Slide 5: Outline
Introduction to datacenter networks
Challenge: Incast problem in datacenter networks
ResQueue: Results
Our proposal: ResQueue
Conclusion
Idea and opportunity

## Slide 6
Many-to-one traffic pattern
  Multiple servers send their data to a single server simultaneously:
    A server sends a query to multiple servers
    Queried servers send their data chunk to the querying server concurrently
  Common in modern datacenter networks
    Social networking, real-time indexing, Web search
  Mostly short flows (e.g., 2 KB)
What is incast?

## Slide 7
Incast aggregator
7
What is incast?

## Slide 8: What is incast?
Port 1
Port 2
Port 3
Q1
Q2
Q3
8
Incast aggregator
Incast + shallow buffers = packet drops

## Slide 9
Many-to-one traffic pattern
  Multiple servers send their data to a single server simultaneously:
    A server sends a query to multiple servers
    Queried servers send their reply to the querying server concurrently
  Common in modern datacenter networks
    Social networking, real-time indexing, Web search
  Mostly short flows
Incast leads to
  Long queues (long tails), packet loss
Incast

## Slide 10
Many-to-one traffic pattern
  Multiple servers send their data to a single server simultaneously:
    A server sends a query to multiple servers
    Queried servers send their reply to the querying server concurrently
  Common in modern datacenter networks
    Social networking, real-time indexing, Web search
  Mostly short flows
Incast leads to
  Long queues (long tails), packet loss
DCTCP performs poorly with incast of short flows (e.g., < 10 KB)
    Both incast duration and incast inter-arrival times are short  no time for rate adjustment
Incast

## Slide 11: Outline
Introduction to datacenter networks
Challenge: Incast problem in datacenter networks
ResQueue: Results
Our proposal: ResQueue
Conclusion
Idea and opportunity

## Slide 12: Idea and opportunity
S2
Short incast duration, short incast inter-arrival time1
  Incasts are highly likely to collide
    Packets are repeatedly dropped
1 High-Resolution Measurement of Data Center Microbursts, [IMC’17]
12

## Slide 13
Q1
Q2
Q3
Incast 1 happens!
Repeated drops!
13
Notes: Here how inter-arrival packets can give u notation about other users.

## Slide 14
Q1
Q2
Q3
Incast 1 happens!
Incast 2 happens!
Repeated drops!
14

## Slide 15: Idea and opportunity
A new study by Facebook1:
  Flows are smaller than what we thought
  ~75% of the flows have only 1 packet
  If incast of 1 KB flows happens:
    Size based flow schedulers will fail
    Congestion control methods cannot help
  If the packet is repeatedly dropped:
      Tail FCT is significantly degraded
1 Inside the Social Network’s (Datacenter) Network [Sigcomm’15]
15

## Slide 16: Idea and opportunity
S2
Maximum drops for any packet in our experiments
16

## Slide 17
DCTCP, ICTCP
Receiver side incast detection (slow)
PIAS
Priority based, does not perform well with same size flows
FastPass, ExpressPass
No flow prioritization (long tails)
Grant-based, wastes bandwidth in some scenarios
NDP
pFabric, PASE
Need apriori knowledge about flow sizes (difficult)
Do not perform well with same size flows
No flow prioritization (long tails)
No flow prioritization (long tails)
Arbiter based, increase latency for short messages
Existing solutions

## Slide 18: Outline
Introduction to datacenter networks
Challenge: Incast problem in datacenter networks
ResQueue: Results
Our proposal: ResQueue
Conclusion
Idea and opportunity

## Slide 19: ResQueue: Design
ResQueue uses a mix of flow size1 and drop history to prioritize packets during incast
  Step I. ResQueue tags packets at the senders, based on number of bytes sent of the corresponding flow
    An illustration of the mechanism:
      If (first_window) -> priority = 1
      If (second_window) -> priority = 2
      If (third_window) -> priority = 3
      If (fourth_window or higher) -> priority = 4
    It uses multi-level queues at switches
      Priority values are based on number of queues in switches
19
1 Information-Agnostic Flow Scheduling for Commodity Data Centers [NSDI’15]

## Slide 20
ResQueue: Design (cont.)
P1
P1
P1
P1
20

## Slide 21
ResQueue: Design (cont.)
P2
P2
P2
P2
P1
21

## Slide 22: ResQueue: Design (cont.)
But step I is not enough
    Almost 75% of short flows have the same size!
      Still a retransmitted packet and a fresh packet both go to priority-1 queue
Step II. Sender server subtracts one from the calculated priority, if and only if the packet is a retransmission
    ResQueue reserves a queue (e.g., priority 0) for retransmitted packets that were part of the first window in previous round
      The reserved queue has the highest priority
      This queue is not shared with other non-dropped packets
    Retransmitted packets belonging to other windows get promoted by one as well
22

## Slide 23
ResQueue: Design
Endhost: priority tagging
Switch
I
N
P
U
T
P
O
R
T
O
U
T
P
U
T
P
O
R
T
Priority-1
If (Retransmitting)
Priority_increase
Priority =
Priority-2
Priority-3
Priority-4
Reserved (high priority-0)
Reserved (high priority-0)
P1
23

## Slide 24
ResQueue: Design
Endhost: priority tagging
Switch
I
N
P
U
T
P
O
R
T
O
U
T
P
U
T
P
O
R
T
Priority-1
If (Retransmitting)
Priority_increase
Priority =
Priority-2
Priority-3
Priority-4
Reserved (high priority-0)
Reserved (high priority-0)
P1
24
P0

## Slide 25: Outline
Introduction to datacenter networks
Challenge: Incast problem in datacenter networks
ResQueue: Results
Our proposal: ResQueue
Conclusion
Idea and opportunity

## Slide 26
Simulation:
  ns-3 simulator
  Leaf-spine topology
    links
    RTT
  Workloads:
    Based on realistic workloads from existing papers
    Various incast degrees between 32 to 48
    Short flow sizes randomly chosen between 1 KB to 10 KB (80% are 1 packet)
    Long flow sizes randomly chosen between 64 KB to 1 MB
Experimental methodology

## Slide 27
Results: Tail (99th %-ile) FCT
ResQueue achieves an average reduction in short flows’ tail FCT by a factor of 1.6x compared to PIAS (load > 60%)

## Slide 28
Results: Throughput
ResQueue achieves an average increase in long flows’ throughput by about 9%, compared to PIAS.

## Slide 29
About 25 KB of reserved buffer is sufficient
  Only a few packets are dropped but they are dropped repeatedly
    Affects tail latency
  It is implementable in super shallow buffers
Results: Reserved buffer’s size

## Slide 30: Conclusion
ResQueue significantly improves short flows’ FCT
  Short flows are scheduled in “priority-1” or “priority-0”
ResQueue improves long flows’ throughput
  It schedules long flows’ retransmitted packets in a higher priority queue
ResQueue does not starve long flows
  Only dropped packets of short flows get high priority
ResQueue compatible with existing congestion control mechanisms
30
Why ResQueue: increasing line rates  buffer pressure in switches will become acute

## Slide 31
  Thank you!